SECTION 09 54 33

WOOD COFFERED CEILINGS

Wood Ceiling Coffers by Madrid, Inc. are a striking solution for beautiful wood ceilings with visual depth. Two styles are available: Dome Coffers made with molded plywood, and Woven Coffers with an attracted woven wood, leather, or metal panel. Coffered panels clip onto a standard suspension grid, providing flush joints and concealing grid.

Specification Coordination: Edit this section to satisfy project requirements and coordinate with work of related sections. This document is available in word processing format at madridinc.com; TURN ON HIDDEN TEXT to view or print notes to specifier.

Drawing Coordination: Show locations of each type of coffer in Drawings or Schedules. Show panel layout, border or perimeter details, and trim. Coordinate above-ceiling work with coffer depth.

Madrid, Inc.
7800 Industry Ave., Pico Riviera, CA 90660
Phone: 562-404-9941, Email: info@madridinc.com. Web: madridinc.com    FSC-C115051

GENERAL

SUMMARY

Section includes ceilings made with wood coffered panels.

Edit list below to include related sections used in specification. Madrid offers woven wood paneling and wood veneer ceiling tiles in finishes to match coffers.

        - Related Sections:

[Section 06 40 23, Interior Architectural Woodwork][06 42 00, Wood Paneling][09 78 00, Interior Wall Paneling]: Woodwork types not specified in this Section.

[Section 09 51 13, Acoustical Panel Ceilings][Section 09 53 00, Acoustical Ceiling Suspension Assemblies]: Suspension system.

Section 09 54 26, Suspended Wood Ceilings: Wood veneer ceiling tiles [to match coffers].

Madrid Inc. produces wood panel ceilings (above) and woven wall and ceiling tiles (below). Guide specifications can be downloaded at www.madridinc.com.

Section 09 78 00, Woven Paneling: Woven wood paneling to match coffers.

REFERENCES

Edit list below to include references used in specification.

ASTM C423: Sound Absorption and Sound Absorption Coefficients by the Reverberation Room Method.

ASTM C635: Metal Suspension Systems for Acoustical Tile and Lay-in Panel Ceilings

ASTM E795: Mounting Test Specimens during Sound Absorption Tests.

ASTM E84: Surface Burning Characteristics of Building Materials.

CISCA Ceiling Systems Handbook.

CISCA Wood Ceilings Technical Guidelines.

Retain below if FSC-certified wood is specified.

[FSC®: Forest Stewardship Council® Chain of Custody Certification.]

ADMINISTRATIVE REQUIREMENTS

Coordinate suspension grid locations with locations of wood coffers.

Coordinate location of penetrations through wood coffers with work of other sections.

To extent practical, schedule installation of wood coffers after work above ceiling is complete.

ACTION SUBMITTALS

Product Data:

Submit manufacturer’s product data sheets and installation instructions.

[Include surface-burning characteristics of intumescent coating.]

Shop drawings are not generally required; retain following only if required for special conditions.

[Shop Drawings: <Insert requirements.>]

Samples for Verification: Provide [two] <other number> 12- by 12-inch corner samples of each wood coffer specified.

Retain below if LEED credit compliance is required; adjust list to reflect credits sought. Credits are based on LEED 2009 NC, Schools, and CS rating systems.

LEED Submittals:

Bamboo veneer and poplar solid wood contribute to credit below.

LEED Credit MR 6, Rapidly Renewable Materials: Product Data indicating percentage by weight of rapidly renewable content for products having rapidly renewable content. Include a statement indicating costs for each product having rapidly renewable content.

Coffers contribute to credit below when specified with FSC-certified wood and veneers.

LEED Credit MR 7, Certified Wood: Chain-of-custody certificates certifying that wood products comply with forest certification requirements. Include evidence that manufacturer is certified for chain of custody by an FSC®-accredited certification body. Include statement of costs for wood products.

LEED Credit EQ 4.4, Low-Emitting Materials: Composite Wood and Agrifiber Products: Documentation indicating that adhesive contains no urea formaldehyde.

QUALITY ASSURANCE

Retain below if FSC Certified wood products are required.

[Manufacturer Qualifications: FSC®"; Chain of Custody Certification.]

Mockups are generally not required. If retained, coordinate with Related Sections.

Mock-up: No fewer than four coffers, showing installation[ and field finishing]. [Accepted mock-up may remain in place in completed Work if undisturbed at Substantial Completion.]

DELIVERY, STORAGE, AND HANDLING

Deliver wood coffers after building is enclosed, concrete, plaster, and drywall work is complete, and HVAC system is operating and maintaining temperature and humidity at occupancy levels.

Store wood coffers in conditioned space. Keep coffers dry.

Conditioning: At least 72 hours before installation, move wood coffers into spaces where they will be installed.

PRODUCTS

MANUFACTURER

Acceptable Manufacturer: Madrid Inc.
Address: 7800 Industry Ave., Pico Riviera, CA 90660
Phone: 562-404-9941
Email: info@madridinc.com
Web: madridinc.com

Substitutions will not be considered.

Select substitution limitation above or below. We are unaware of another manufacturer that offers a clip equivalent to our coffer clip. Consider specifying Madrid as only acceptable manufacturer.

Substitutions will be considered according to [Instructions to Bidders.][Division 01 Requirements.]

SUSPENSION SYSTEM

Coordinate with suspension system in Part 1 article “Related Sections”.

Provide 15/16 inch wide suspension system complying with ASTM C635 and as specified in Related Section.

PANELS – GENERAL

Retain option in paragraph below if FSC certification is required.

        - Materials: [Provide FSC® certified wood products].

Other species are available upon request.

Solid Wood: [Steamed beech.]<Insert other species>

Molded Plywood, made with no added urea formaldehyde.

Face Veneer:

For multiple veneer choices, indicate locations or patterns in Drawings. For paint-grade coffers, omit veneer requirements.

[Plain][Rift] sliced oak.

[Plain][Quarter] sliced cherry.

[Plain][Quarter] sliced maple.

[Plain][Quarter] sliced mahogany.

Natural bamboo, wide strips.

Dark bamboo, wide strips.

<Insert veneer from custom options; see madridinc.com.>

Madrid’s coffer clip system allows removal of individual coffers with simple tools. While coffers require no additional clearance, coordinate tolerances and installation requirements of construction above to prevent conflicts.

        - Attachment:

Clip: Panels shall have clip to snap coffer to face of suspension grid, allowing installation without special tools.

          - Joint: Butt joint, concealing suspension grid.

          - Above-Ceiling Access: Downward non-progressive removal of individual panels.

Product: McMaster Carr; hook 7426A32. Phone: 609-689-3415.

Provide [two]<insert number> tools for removing individual panels.

          - Clearance: No clearance required between top of coffer and work above.

        - Face Dimensions:

Coffered Panels: Nominal 24 by 24 inches.

Perimeter Panels: As indicated in Drawings.

        - Panel Edges: Solid wood.

Adhesives: No added urea formaldehyde.

Fabrication Tolerances: Complying with CISCA Wood Ceilings Technical Guidelines.

Retain following with Dome Coffers; edit to reflect project requirements.

      - DOME COFFER PANELS

        - Product: Domed Wood Ceiling Coffers by Madrid, Inc.

        - Configuration:

Frame: Solid wood.

Dome: Veneer-faced molded plywood.

        - Height: 3 3/4 inches above bottom face of suspension grid; 1/2 inch below suspension grid.

        - Weight: 3.0 lb. per square foot maximum.

Retain dome coffers (above) or woven coffers (below). If both types are required, show locations in Drawing or Schedules.

      - WOVEN COFFER PANELS

        - Product: Weave Wood Ceiling Coffers by Madrid, Inc.

Configuration:

Frame: Solid wood, 1 3/4 inches wide.

Concave Molding: Solid wood, 3 3/4 inches wide.

Select one or more woven inserts from next three subparagraphs. For multiple panel choices, indicate locations in Drawings.

Woven Wood Insert: Veneer-wrapped bent wood strips with flat faces, 1.5 inches wide, nominal 1.5 inches on center, 0.5 inches thick overall. Monolithic tiles or panels are not acceptable. Align veneer grain with long edge of woven strips.

Select one or more veneers from list below or from broad selection at www.madridinc.com. For multiple veneer choices, indicate locations or patterns in Drawings.

[Plain ][Rift ]sliced oak.

[Plain ][Quarter ]sliced cherry.

[Plain ][Quarter ]sliced mahogany.

<Insert veneer from custom options; see www.madridinc.com.>

Woven Leather Panel: Leather-wrapped bent wood strips with flat faces, 1.5 inches wide, nominal 1.5 inches on center, 0.5 inches thick overall.

Contact Madrid for leather recommendations.

            - Leather Cladding: <Insert leather requirements>.

Select a finish from options below.

          - Woven Metal Panel: Cast aluminum simulated woven strips, 1.5 inches wide and nominal 1.5 inches on center, with electroplated [copper ][antique bronze ][satin nickel ]finish.

Acoustical backing is optional for wood and leather woven panels. Contact Madrid for recommendations for optimizing absorption to suit project.

Noise Reduction: Wood coffered ceiling shall provide NRC of [0.60][0.50]<Insert requirement> per ASTM C423 with ASTM E795 Type E-400 mounting.

        - Height: 3 3/4 inch height above bottom face of suspension grid; 1/2 inch below suspension grid.

        - Weight: 3.0 lb. per square foot maximum.

Perimeter panels can be cut to size required and used as a border around coffered panels. Show width of border on Drawings.

PERIMETER PANELS

Flat Panels:

Product: Wood Ceiling Tiles by Madrid, Inc.

Select core from list below. Select recycled fiber core for its environmental qualities, or MDF or particleboard for lower cost. Select fire-treated MDF if Class A surface is required. Retain FSC-Certified substrate if required.

Core: One of following:

MDF: ANSI A208.2, Grade 130. Fire-treated. [FSC® Certified.]

Particle board: ANSI A208.1 Grade M-2. [FSC®Certified.]

Face Veneer: Align grain [[parallel] [perpendicular] to edge of ceiling; miter veneer on corner panels.] [as shown on Drawings.]

Woven Panels:

Product: Fabricated from Weave tiles by Madrid, Inc.

Tiles shall match woven inserts specified for woven coffers.

If  woven panels are described elsewhere in this Section, use above. Otherwise, use below.

Tiles:

Pattern: Woven strips 1.5 inches wide and 1.5 inches on center.

Woven Wood: Veneer-wrapped bent wood strips with flat faces, 1.5 inches wide, nominal 1.5 inches on center, 0.5 inches thick overall. Monolithic tiles or panels are not acceptable. Align veneer grain with long edge of woven strips.

Select one or more veneers from list below or from broad selection at www.madridinc.com. For multiple veneer choices, indicate locations or patterns in Drawings.

[Plain ][Rift ]sliced oak.

[Plain ][Quarter ]sliced cherry.

[Plain ][Quarter ]sliced mahogany.

<Insert veneer from custom options; see www.madridinc.com.>

Woven Leather Panel: Leather-wrapped bent wood strips with flat faces, 1.5 inches wide, nominal 1.5 inches on center, 0.5 inches thick overall.

Contact Madrid for leather recommendations.

Leather Cladding: <Insert leather requirements>.

Select a finish from options below.

            - Woven Metal Panel: Cast aluminum simulated woven strips, 1.5 inches wide and nominal 1.5 inches on center, with electroplated [copper ][antique bronze ][satin nickel ]finish.

Apply woven tiles to a backer sheet.

Orient woven tiles [parallel] [at 45 degree angle] to edges of panel.

FACTORY-APPLIED FINISHES

Madrid recommends field staining and finishing wood when matching of adjacent finishes is critical. For factory-finished panels, retain below.

Transparent Finish:

Stain solid wood to match [veneer.] [color selected by Architect.]

Apply transparent, water-based, UV-cured matte finish to exposed wood.

[Fire Resistant Treatment: Factory-applied transparent intumescent coating providing 25 maximum flame-spread and 200 maximum smoke-developed per ASTM E84.]

Retain below for factory priming for field painting.

Primer: Prime for field painting.

FABRICATION

To extent practical, factory cut holes for [lighting,] [fire sprinklers,] [speakers,] [and other] panel penetrations.

ACCESSORIES

Madrid Wood Coffers are designed to conceal suspended grid and edge moldings without additional applied trim. If exposed trim is required, indicate type and profile in Drawings. Solid wood and veneered trims are available from Madrid to match or coordinate with coffers.

Trim: [Match veneer and finish of coffers, in profile shown in Drawings.][See related sections for trim supplied as part of suspension system.]

Acoustical insulation installed above Wood Weave Coffers can improve noise absorption (NRC).

Acoustical Insulation: <Insert requirements.>

For field-finished panels requiring Class A flame spread, retain below.

Fire-Resistant Treatment: Clear field-applied intumescent coating formulated for application over transparent-finished wood, providing 25 maximum flame-spread and 200 maximum smoke-developed per ASTM E84.

Available Product: Envirograf; Q/VFR/Premier/Clear, [matte ][satin ][gloss].

EXECUTION

EXAMINATION

Verify that suspension grid is acceptable for installation of panels.

INSTALLATION

Install panels according to manufacturer's instructions and CISCA Ceiling Systems Handbook.

Snap panels into place onto face of suspension grid.

Add requirements for trim, acoustical insulation, and field finishing below. Delete paragraphs not required.

Trim: <Insert requirements.>

Acoustical Insulation: <Insert requirements.>

Field Finishing: <Insert requirements.>

CLEANING AND PROTECTION

Clean panels as recommended by manufacturer.

Prevent damage to panels during remainder of construction period.

END OF SECTION

Copyright 2012 by Madrid, Inc. Qualified design and construction professionals may copy for preparation of construction specifications. Issued July 2012.